EPS Template

DER 6-32.8-xxxx_Ayy

Author: J.v.Engelen

Date: 95/02/21

Any other comment

For the EPS template the following nomenclature should be used in document file names and document numbers:

xxxx represents the project number (i.e. PSxxxx = PS0186) or the

sub-system (i.e. xxxx = IAD_) the document belongs to.

A is reserved for EPS documents

yy is just a sequence number free to choose.

nnn is the version where the project number is implemented.

# EPC-8/8A BIOS settings for VMEbus CNC

# PS0691

copy: Mr.	T. Veldhoven, HEIDENHAIN NUMERIC Eindhoven

M. Ziegler, Deckel Maho

R. Glaser, HEIDENHAIN Servicestelle Fellbach

File		: 0691_z04.wp

Status		: Final

Version	: 10.0

1.  History	1

2.  Introduction	1

2.1  Purpose	1

2.2  Scope	1

2.3  Definitions, Acronyms and Abbreviations	1

3.  General Description	3

3.1  Entering the BIOS set-up function and moving around	3

3.2  BIOS settings	3

3.2.1  Main menu	4

3.2.1.1  IDE adapter 0 Master sub-menu	4

3.2.1.2  IDE adapter 1 Master sub-menu	5

3.2.1.3  Boot option sub-menu	5

3.2.1.4  Keyboard Features sub-menu	6

3.2.2  Advanced Menu	6

3.2.2.1  Integrated peripherals sub-menu	7

3.2.2.2  Memory Shadow sub-menu	7

3.2.3  EXM menu	7

3.2.4  VME Menu	8

3.2.5  Exit Menu	9

4.  References	10

Start of Text

1.  History

| Date | Author | DCR | Change description |
| --- | --- | --- | --- |
| 25-8-95 | Walter Scheepens |  | First draft |
| 2-12-95 | Walter Scheepens |  | Settings for 80 MB hard disk added. 200 MB HD settings will follow |
| 7-12-95 | Walter Scheepens |  | 200 MB HD BIOS settings added |
| 6-3-96 | Walter Scheepens |  | 500 MB HD BIOS settings added. Formatted to only 285 Mbyte due to restrictions in the disk driver in the CNC SW |
| 20-1-97 | Walter Scheepens |  | 500 MB HD now fully used. From Mill Plus/ CNC Pilot V311/00 no restrictions for HD size in disk driver |
| 1-1-97 | Walter Scheepens |  | 1.4 GB HD BIOS settings added. Mill Plus/ CNC Pilot with C=20MB, D=1250MB (E=220MB Not formatted) |
| 17-11-98 | Ton Veldhoven |  | 2.1 GB HD BIOS settings added. Mill Plus/CNC Pilot with C=20MB D=1900MB (E=241MB Not formatted) |
| 12-02-02 | Ton van der Heijden |  | 6.0 GB HD BIOS settings added. Mill Plus/CNC Pilot with C=50MB, D=1900MB en E=1900MB. Hard disk formatted with upgraded format file (version2.0). Using this format file for formatting the previous HD’s will also increase the C-drive from 20MB into 50MB |
| 2-3-04 | Ton van der Heijden |  | Option Byte 1 of EXM Slot 31 changed from [00] into [01] |
| 20-10-04 | Ton Veldhoven |  | Used Disk higher then 3Gbyte |

2.  Introduction

# This document describes the EPC-8 BIOS settings required for the VMEbus CNC configurations. Since the EPC-8A is the successor of the EPC-8, everywhere in this document EPC-8 is written, also

EPC-8A can be read.

2.1  Purpose

For a VMEbus system to function correctly, the BIOS settings must be set as described in this document. The BIOS settings can be changed using the built-in BIOS set-up function. BIOS setup is required:

1.	During production (system assembly and software installation)

2.	Replacement of a faulty EPC-8 (service)

3.	After replacing a dead battery

2.2  Scope

BIOS setup is required for VMEbus CNC systems, V30X, V31X, V32X, V33X, V35X, V36X, V37X, V40X, V41X and V42X. The BIOS setup menus are described for the EPC-8 BIOS from version 1.02.02.

2.3  Definitions, Acronyms and Abbreviations

BIOS		Basic I/O System.

DOS		Disk Operating System

ECP		Extended Capabilities Parallel port

EGA		Extended Graphics Adapter

IDE		Intelligent Drive Electronics

LBA		Logical Block Addressing

POST		Power On Self Test

ROR		VMEbus Release On Request

RONR		VXIbus Release On No Request

ULA		VXI Upper Logical Address register

VGA		Video Graphics Adapter

VME		Versa Module Euro-format

VXI		VMEbus eXtensions for Instrumentation

3.  General Description

3.1  Entering the BIOS set-up function and moving around

To use the BIOS set-up function built-in the EPC-8, a PC keyboard must be connected to the EPC-8  front panel (Bottom connector, miniD).

The BIOS setup is activated when after resetting the system (reset push button on front panel of the EPC-8) or after power-on the "F2" key on the PC keyboard is depressed. The simplest way to do this is to reset and keep "F2" depressed until the BIOS set-up is activated.

The BIOS setup comes up with a blue and grey screen, where the user can move around using the cursor keys. The cursor left and right keys moves between the menu entries in the menu (the blue horizontal bar in the top of the screen), the cursor up and down move between the set-up variables on one page. The selected variable is highlighted. The variables can be changed by either hitting the space bare once or more times or by using the "+" and "-" keys. Numeric variables can be changed by typing the numeric value.

Some items are marked with a ►, which indicates that a sub-menu is hiding beneath this item. Hitting the Enter key when the cursor is moved on top of the item enters this sub-menu. Sub-menus can be left by pressing the Esc key.

The BIOS set-up is terminated by moving the cursor to EXIT in the main menu by using the cursor right keys or hitting the Esc key once or twice. On EXIT press Enter and again Enter when a message box pops up.

3.2  BIOS settings

The BIOS set-up main menu has 5 pages, which can be reached by moving the cursor left or right to the main menu entries, displayed on the horizontal menu bar: Main, Advanced, EXM, VME or Exit.

The menus described below are valid for the BIOS versions from version 1.02.02. Older BIOS versions do not have all of the items shown below.

There are several VMEbus CNC hardware configurations, which will have a different BIOS setup setting. The configurations discussed here are:

# 1.	CNC pilot 1250 and 1290 (without hard disk)

This configuration has an EPC-8 with an EXM2A memory extension module (EXM slot 0) and an EXM-8 ControlNet module (EXM slot 1)

# 2.	CNC pilot 1290 (with 80 MB, 200 MB, 500 MB, 1.4 GB, 2.1 GB, 6 GB or 30 GB hard disk)

This configuration has an EPC-8 with an EXM-HD hard disk module (EXM slot 0) and an EXM-8 ControlNet module (EXM slot 1).

Note: The EPC-8A functions only in combination with an EXM-8A.

# 3.	Manual Plus

This configuration has an EPC-8 only.

3.2.1  Main menu

The main menu has the following contents. The settings should be as shown. When not change the settings as described above.

# RadiSys EPC-8

System Time:			[14:52:11]		<< current time is shown here

System Date:			[20/06/2001]		<< current date is shown here

Diskette A:			[Not installed]

Diskette B:			[Not installed]

►	IDE adapter 0 Master:		(none)			<< with a HD, this will show disk size

<< after submenu has been filled (Note)

►	IDE adapter 0 Slave:		(none)

Video System:			EGA / VGA]

►	Boot sequence:			[C: only]

►	Numlock:			[Auto]

System Memory			640 KB

Extended Memory			7168 KB / 15360 / 31744 KB

The BIOS setup items marked with ► lead to sub-menus when Enter is pressed and the cursor is placed on the item. These sub-menus are described in the following sub-sections. One can return to the main menu by depressing the Esc key.

Note : for BIOS versions <4.05, autotype detects the specifications for the 6.0 GB hard disk filled in according to 3.2.1.1 but displays the value 1712MB.

Therefore don’t use autotype Fixed Disk.

3.2.1.1  IDE adapter 0 Master sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "IDE adapter 0 Master". The following text is displayed. Shown are the settings as they should be for the various system configurations: The first table shows the settings for a system without hard disk. The second table depicts the settings for systems with hard disk with a size of 80MB, 200 MB, 500 MB, 1.4 GB, 2.1 GB  6 GB and 30 GB respectively.

Flash disk (1250, 1290 no HD,

Manual Plus

IDE adapter 0 Master

Autotype Fixed Disk		[Press Enter]

Type:				[none]

Cylinders:

Heads:

Sectors / Track:

Write Precompensation:

LBA Mode Control:		[Disabled]

Hard disk 80 MB	Hard disk 200MB	Hard disk 500MB

(1290 with HD)	(1290 with HD)		(1290 with HD)

(Note1)

# IDE adapter 0 Master

Autotype Fixed Disk		[Press Enter]		[Press Enter]		[Press Enter]

Type:				[user]			[user]			[user]

Cylinders:			[966]			[723] 			[1053] (Note1)

Heads:				[5]			[11]			[16]

Sectors / Track:		[34]			[63]			[63]

Write Precompensation:	[none]			[none]			[none]

LBA Mode Control:		[Disabled]		[Disabled]		[Disabled]

Note 1: Some 500 Mbyte hard disks have been formatted to 285 Mbyte due to limitations in the disk

drive software in Mill Plus/CNC Pilot 1290 V310. These disks have the Cylinders parameter set to 550.

Hard disk 1.4 GB	Hard disk 2.1 GB	Hard disk 6.0 GB

(1290 with HD)	(1290 with HD) 	(1290 with HD)

(Note 2)		(Note3)			(Note4)

# IDE adapter 0 Master

Autotype Fixed Disk		[Press Enter]		[Press Enter]		[Press Enter]

Type:				[user]			[user]			[user]

Cylinders:			[2792]			[4188] 			[12416]

Heads:				[16]			[16]			[15]

Sectors / Track:		[63]			[63]			[63]

Write Precompensation:	[none]			[none]			[none]

LBA Mode Control:		[Disabled]		[Disabled]		[Disabled]

Hard disk 30 GB

(1290 with HD)

(Note5)

# IDE adapter 0 Master

Autotype Fixed Disk		[Press Enter]

Type:				[user]

Cylinders:			[6349]

Heads:				[16]

Sectors / Track:		[63]

Write Precompensation:	[none]

LBA Mode Control:		[Enabled]

Note 2:	 1.4 Gbyte hard disks have been formatted to 1270Mbyte ( Drive C= 20MB and D= 1250MB ).

Note 3:	 2.1 Gbyte hard disks have been formatted to 1920Mbyte ( Drive C= 20MB and D= 1900MB ).

Note 4:	 6.0 Gbyte hard disks have been formatted to 3276Mbyte ( Drive C= 50MB and D= 1900MB ).

Note5 :	 30 Gbyte hard disks have been formatted to 3276Mbyte ( Drive C= 50MB, and D= 1900MB ).

Used the correct Setup flop Version 4.3 to formatted the disk (No E drive is formatted).

3.2.1.2  IDE adapter 1 Master sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "IDE adapter 1 Master". The following text is displayed. Shown are the settings as they should be.

# IDE adapter 1 Master

Autotype Fixed Disk		[Press Enter]

Type:				[none]

Cylinders:

Heads:

Sectors / Track:

Write Precompensation:

LBA Mode Control:		[Disabled]

3.2.1.3  Boot option sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "Boot Sequence". The following text is displayed. Shown are the settings as they should be.

# Boot Options

Boot delay:			[0]

Boot sequence:			[C: only]

SETUP prompt:		[Disabled]

POST errors:			[Disabled]

Floppy Check:			[Disabled]

Summary Screen:		[Disabled]

3.2.1.4  Keyboard Features sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "Numlock". The following text is displayed. Shown are the settings as they should be.

# Keyboard Features

Numlock:			[Auto]

Key Click:			[Disabled]

Keyboard auto-repeat rate:	[30 / sec]

Keyboard auto-repeat delay:	[ sec]

3.2.2  Advanced Menu

The Advanced  menu has the following contents. The settings should be as shown. When not, change the settings using the procedure as described above. Two settings are shown: Column 1 for systems  without hard disk and column 2 for systems with hard disk.

Flash disk			Hard disk

(1250, 1290 no HD,		(1290 with HD)

Manual Plus

RadiSys EPC-8

►	Integrated Peripherals

►	Memory Shadow

Halt on Watchdog Timer:	[Disabled]			[Disabled]

Large Disk Access Mode:	[DOS]				[DOS]

Built-in BIOS Extension Configuration

BIOS extension Addresses

Flash ROMdisk:		[C800-CBFFh]		[Not Installed]

Serial Flash Recovery:	[CC00-CFFFh]		[Not Installed]

VME ROMdisk:		[Not Installed]			[Not Installed]

VME can Range:		[0 - FFF00000    A32]	[0 - FFF00000    A32]

There are two sub-menus in the Advanced menu. They can be entered by pressing Enter when the cursor is placed on the sub-menu selection line.

3.2.2.1  Integrated peripherals sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "Integrated Peripherals". The following text is displayed. Shown are the settings as they should be.

# Integrated Peripherals

# COM1:		[3F8, IRQ4]

COM2:		[2F8, IRQ3]

LPT1:			[378, IRQ7]

ECP:			[Disabled]

3.2.2.2  Memory Shadow sub-menu

This sub-menu is selected when the enter is pressed with the cursor on "Memory Shadow". The following text is displayed. Shown are the settings as should be.

# Memory Shadow

System Shadow	Enabled

Video Shadow		Enabled

Shadow Memory Regions:

C800 - CFFF:		[Disabled]

CC00 - CFFF:		[Disabled]

D000 - D3FF:		[Disabled]

D400 - D7FF:		[Disabled]

D800 - DBFF:		[Disabled]

DC00 - DFFF:		[Disabled]

3.2.3  EXM menu

The EXM menu is entered by pressing the right/left cursor keys until the cursor is on EXM in the menu bar. The following text is displayed. Shown are the settings for three CNC configurations: Column 1, with an EPC-8 and two EXM modules (in one VMEbus slot): EXM-8 (ControlNet) and EXM2A (SRAM/Flash expansion). Column 2 for configurations with an EXM-HD hard disk module instead of the SRAM/Flash expansion module. Column 3 for the Manual Plus configuration which has no EXM modules at all.

Flash disk		Hard disk		Flash disk

(1250, 			(1290 with HD)		(Manual Plus)

1290 no HD)

RadiSys EPC-8

# EXM Slot 31

ID:				[FD]			[FD]			[FD]

Option Byte 1:		[01]			[01]			[01]

Option Byte 2:		[00]			[00]			[00]

EXM Slot 0

ID:				[FD]			[7D]			[FF]

Option Byte 1:		[00]			[05]			[00]

Option Byte 2:		[00]			[00]			[00]

EXM Slot 1

ID:				[F7]			[F7]			[FF]

Option Byte 1:		[A1]			[A1]			[00]

Option Byte 2:		[11]			[11]			[00]

EXM Slot 2

ID:				[FF]			[FF]			[FF]

Option Byte 1:		[00]			[00]			[00]

Option Byte 2:		[00]			[00]			[00]

EXM Slot 3

ID:				[FF]			[FF]			[FF]

Option Byte 1:		[00]			[00]			[00]

Option Byte 2:		[00]			[00]			[00]

EXM Slot 4

ID:				[FF]			[FF]			[FF]

Option Byte 1:		[00]			[00]			[00]

Option Byte 2:		[00]			[00]			[00]

EXM Slot 5

ID:				[FF]			[FF]			[FF]

Option Byte 1:		[00]			[00]			[00]

Option Byte 2:		[00]			[00]			[00]

3.2.4  VME Menu

The VME menu is entered by pressing the right/left cursor keys until the cursor is on VME in the menu bar. The following text is displayed. Shown are the required settings.

# RadiSys EPC-8

Arbitration Priority:		[0]

Arbitration Mode:		[Round Robin]

Bus Release:			[RONR (VXI)]

ULA:				[00]

3.2.5  Exit Menu

The Exit menu is entered by pressing the right/left cursor keys until the cursor is on EXIT in the menu bar. The following text is displayed. No variables are set here, but various modes can be selected

# RadiSys EPC-8

# Save values and Exit

Discard Values and Exit

Get Default Values

Load Previous Values

Save Current values

Exit & Update BIOS

Do not select the last menu item, unless you have an EXM disk unit with floppy disk drive in EXM slot 0 and a BIOS floppy.

4.  References

1.	EPC-8 Hardware Reference Manual. RadiSys.